## Slide 2: Closed Circuit Coolers
The cooling fluid through the coil
Spray water over the coil
Air flow is counter flow to spray water
Heat transferred through the coil wall to spray water
Heat is rejected by evaporation of portion of spray water
Principle of operation
Hot Water
In
Hot Saturated Discharge Air
Cool Dry
Entering Air
Notes: This is a diagram of the heat removal process of a closed circuit cooler. This is an in-direct cooling process, and has many more benefits to the owner which we will discuss.

## Slide 3: Example Applications: Chillers

## Slide 4: Example Applications: Heat Pumps

## Slide 5: Closed Circuit Coolers
Closed System:
  Will not foul heat exchanger surfaces
  Will not contaminate process cooling equipment
  Reduced maintenance costs condenser system and chiller
Higher Fluid Temperature Limitations (Maximum fluid temperature of 75°C)
Application advantages

## Slide 6: Closed Circuit Coolers
Dry Operation Option (except ESWA & ESWB) :
  Reduce water consumption
  Avoid potential freezing problems during the winter
Application advantages (cont.)

## Slide 7: Closed Circuit Coolers
Dry Operation Option (except ESWA & ESWB) :
  Reduce water consumption
  Avoid potential freezing problems during the winter
Plume abatement solutions
Application advantages (cont.)

## Slide 8: Induced Draft with Axial Fans
EVAPCO Closed Circuit Coolers Product line

## Slide 9: Induced Draft with Axial Fans
ATW
ESWA/B

## Slide 10: Induced Draft Closed Circuit Coolers with Axial Fan : ATW
Hot Satured Discharge Air
Hot Water In
Cooled Water Out
Cool Dry Entering Air
377 models
25 – 6200 kW
1 – 267 l/s

## Slide 11: Induced Draft Closed Circuit Coolers with Axial Fan : ESWA
Combination of coil and fill technology
179 models
264 – 5120 kW
11,4 – 234 l/s
Hot Satured Discharge Air
Cool Dry Entering Air
Cool Dry Entering Air
Cooled Fluid Out
Hot Fluid In

## Slide 12: Induced Draft Closed Circuit Coolers with Axial Fan : ESWB
Combination of coil and fill technology
Maximum capacity per m² footprint
599 models
171 – 2129 KW
7,4 – 92 l/s
Hot Satured Discharge Air
Cool Dry Entering Air
Cool Dry Entering Air
Cooled Fluid Out
Hot Fluid In
Redistribution Basin

## Slide 13
Forced Draft with Centrifugal Fans
EVAPCO Closed Circuit Coolers Product line

## Slide 14: Forced Draft with Centrifugal Fans
LRW
LSWA

## Slide 15: Forced Draft Coolers with Centrifugal Fan : LSWA
50 models
73 – 2673 kW
3,1 – 115 l/s

## Slide 16: Forced Draft Closed Circuit Coolers with Centrifugal Fan : LRW
Low height applications
38 models
43 – 58 kW
7,7 – 25 l/s

## Slide 17: Comparison Different CCC Solutions
Type | Relative cost |  | Fan Motor |  |  | Pump Motor |  |  | Total kW
ATW | 124% |  | 2 | 22 |  | 2 | 2,2 |  | 48,4
 | 130% |  | 2 | 15 |  | 2 | 2,2 |  | 34,4
ESWA | 100% |  | 1 | 15 |  | 1 | 7,5 |  | 22,5
ESWB | 120% |  | 1 | 18,5 |  | 1 | 7,5 |  | 26
LSWA | 125% |  | 1 | 37 |  | 1 | 5,5 |  | 42,5
Example: 1000 kW (35 - 29,44 - 25,56°C)

## Slide 18: Comparison Different CCC Solutions
Type | Relative cost |  | Fan Motor |  |  | Pump Motor |  |  | Total kW
ATW | 124% |  | 2 | 22 |  | 2 | 2,2 |  | 48,4
 | 130% |  | 2 | 15 |  | 2 | 2,2 |  | 34,4
ESWA | 100% |  | 1 | 15 |  | 1 | 7,5 |  | 22,5
ESWB | 120% |  | 1 | 18,5 |  | 1 | 7,5 |  | 26
LSWA | 125% |  | 1 | 37 |  | 1 | 5,5 |  | 42,5
Example: 1000 kW (35 - 29,44 - 25,56°C)

## Slide 19
EVAPCO Closed Circuit
HYBRID Coolers Product line

## Slide 20
Notes: In this slide, we can see all the hybrid units together. Units which have been developed to increase the dry performance to save water and when possible to save energy. Save water means not only propose an evaporative unit which let the customer to reduce the water itself, but also a unit which take the customer to spend less money for all the costs connected to the consuption of water: chemical cost, sewer cost etc
--
You know we can offer centrifugal and axial units, so EVAPCO is able to supply all the possible solutions for all the project where an evaporative unit is required to save water and energy (when it is possible)

## Slide 21: Dry operation - Save water Plume abatement
EVAPCO Closed Circuit
HYBRID Coolers Product line

## Slide 22: Induced Draft with Axial Fans
EVAPCO Closed Circuit
HYBRID Coolers Product line

## Slide 23: Induced Draft with Axial Fans
eco-ATWB
eco-ATWB-H
eco-ATWB-E

## Slide 24: Hybrid Closed Circuit Coolers with Axial Fans: eco-ATWB
CROSSCOOLTM
Ellipti-fin®:Extended surface coil
Excellent dry switch points

## Slide 25: Hybrid Closed Circuit Coolers with Axial Fans: eco-ATWB
704 models
42 – 10810 kW
1,8 – 466 l/s

## Slide 26: Hybrid Closed Circuit Coolers with Axial Fans: eco-ATWB-E
CROSSCOOLTM
Ellipti-fin®: Extended surface coil
Hybrid operation possible
Reduced Water Consumption

## Slide 27: Hybrid Closed Circuit Coolers with Axial Fans: eco-ATWB-E
228 models
377 – 2630 kW
16,3 – 113 l/s

## Slide 28: Hybrid Closed Circuit Coolers with Axial Fans: eco-ATWB-H
CROSSCOOLTM
Ellipti-fin®
ARID-fin PakTM: Dry cooling coil
Hybrid operation
Maximum dry switch points
Optimized technology for increased water savings
Plume abatement

## Slide 29: Hybrid Closed Circuit Coolers with Axial Fans: eco-ATWB-H
2036 models
250 – 4895 kW
10,8 – 211 l/s

## Slide 30: Forced Draft with Centrifugal Fans
EVAPCO Closed Circuit
HYBRID Coolers Product line

## Slide 31: Hybrid Forced Draft with Centrifugal Fans
LSWA-H
LRW-H

## Slide 32: Hybrid Closed Circuit Coolers with Centrifugal Fans: LSWA-H
ARID-fin PakTM: Dry cooling coil
High dry switch points
Hybrid operation
Reduced water consumption
Plume abatement

## Slide 33: Hybrid Closed Circuit Coolers with Centrifugal Fans: LSWA-H
ARID-fin PakTM: Dry cooling coil
215 models
73 – 2673 kW
3,1 – 115 l/s

## Slide 34: Hybrid Closed Circuit Coolers with Centrifugal Fans: LRW-H
ARID-fin PakTM: Dry cooling coil
High dry switch points
Hybrid operation
Reduced water consumption
Plume abatement

## Slide 35: Hybrid Closed Circuit Coolers with Centrifugal Fans: LRW-H
ARID-fin PakTM: Dry cooling coil
91 models
43 – 580 kW
1,9 – 25 l/s

## Slide 36: Comparison Different Hybrid Models
Type | Relative cost |  | Fan Motor |  |  | Pump motor |  |  | Total kW
eco ATWB | 100% |  | 1 | 30 |  | 1 | 5,5 |  | 35,5
 | 112% |  | 1 | 18,5 |  | 1 | 5,5 |  | 24
eco ATWB E | 170% |  | 1 | 30 |  | 2 | 2,2 |  | 34,4
 | 173% |  | 1 | 15 |  | 2 | 2,2 |  | 19,4
eco ATWB H | 191% |  | 1 | 15 |  | 1 | 5,5 |  | 20,5
LSWA - H | 149% |  | 2 | 37,5 |  | 1 | 5,5 |  | 80,5
Example: 1000 kW (35 - 29,44 - 25,56°C)

## Slide 37: Hybrid Solutions – Comparison Dry Operation
Type | Relative cost |  | Fan Motor |  |  | Pump motor |  |  | Total kW |  | Dry Switch Point
eco ATWB | 100% |  | 1 | 30 |  | 1 | 5,5 |  | 35,5 |  | +4,1°C
 | 112% |  | 1 | 18,5 |  | 1 | 5,5 |  | 24 |  | 
eco ATWB E | 170% |  | 1 | 30 |  | 2 | 2,2 |  | 34,4 |  | +4,2°C
 | 173% |  | 1 | 15 |  | 2 | 2,2 |  | 19,4 |  | 
eco ATWB H | 191% |  | 1 | 15 |  | 1 | 5,5 |  | 20,5 |  | +11,2°C
LSWA - H | 149% |  | 2 | 37,5 |  | 1 | 5,5 |  | 80,5 |  | +11,84°C
Example: 1000 kW (35 - 29,44 - 25,56°C)

## Slide 38: Know Your Options
EVAPCO Closed Circuit Coolers