## Slide 2
Open Type
Counterflow Cooling Towers
EVAPCO EUROPE BVBA

## Slide 3: Principle of Operation
Hot Saturated Discharge Air
Cool, Dry Air
Counterflow Cooling Towers
Notes: 3

## Slide 4
Design Advantages
&
Product Features
Counterflow Cooling Towers

## Slide 5
Thermal Performance Certification
Eurovent and CIT Certification: Capacity Guaranteed
Counterflow Cooling Towers

## Slide 6
EVAPCO Cooling Towers…designed to
withstand seismic or wind load forces
IBC Compliant Design
Counterflow Cooling Towers

## Slide 7
What is IBC?
  The International Building Code requires that equipment must meet the same seismic or wind load forces as the building to which they are attached
How Does it Apply?
  Based on project location and site design factors, calculations are made to determine the equivalent seismic “g force” and wind load on the unit
IBC Compliant Design
Counterflow Cooling Towers

## Slide 8
What does EVAPCO offer?
  Standard Structural Design
    Projects with ≤ 1.0g seismic or 60psf wind loads
  Upgraded Structural Design for high seismic and wind loads area
IBC Compliant Design
Counterflow Cooling Towers

## Slide 9
Independent, 3rd Party Certification
IBC Compliant Design
Counterflow Cooling Towers

## Slide 10
Counterflow Cooling Towers
AT
Induced Draft
Hot Saturated Discharge Air
Cool Dry Entering Air
Hot Water In
Cooled Water Out
LSTE
Forced Draft
Hot Saturated Discharge Air
Cool Dry Entering Air
Hot Water In
Cooled Water Out

## Slide 11: Cooling Tower Hygiene
Eurovent 9/7
RECOMMENDED CODE OF PRACTICE TO KEEP YOUR COOLING SYSTEM EFFICIENT AND SAFE
Maintaining System Efficiency
Maintaining Equipment Safety
Annexe 1: Water Quality Requirements
Annexe 2: Cooling System Logbook

## Slide 12
AT
Induced Draft
Counterflow Cooling Towers

## Slide 13: Product Range – AT/UAT Cooling Towers
Advanced Technology
Ultra AT-
Full Stainless Steel
AT Induced Draft Counterflow Cooling Towers
139 – 22.100 kW

## Slide 14: Nomenclature - AT/UAT Cooling Towers
AT-112-3N14
AT Induced Draft Counterflow Cooling Towers
AT | - | Advanced Technology
1 | - | # of Cells
12 | - | Width of Unit (feet)
3 | - | Capacity Designator
N | - | Motor Size
14 | - | Length of Unit (feet)

## Slide 15
EVAPCO Corrosion Protection System
Z725 Galvanized Steel
PVC Distribution System
PVC Inlet Louvers
PVC Drift Eliminators
Stainless Steel Strainers
Signature Features – Materials of Construction
AT Induced Draft Counterflow Cooling Towers

## Slide 16
  725 g of Zinc per m²
  Highest in Industry
Superior Corrosion Protection !
Signature Features – Z-725 Hot Dip Galvanized Steel
Counterflow Cooling Towers

## Slide 17
Advanced Material Option
Stainless Steel Lower Section
Type 304L and Type 316L Stainless Steel
Signature Features – Materials of Construction
Stainless Steel
AT Induced Draft Counterflow Cooling Towers

## Slide 18
Advanced Material Option
Type 304L Stainless Steel Casing and Fan Deck
Type 316L Stainless Steel Basin
316L SS
304L SS
Signature Features – Materials of Construction
AT Induced Draft Counterflow Cooling Towers

## Slide 19
Signature Features – Materials of Construction
Advanced Material Option
Complete 316L SS Construction
100% Corrosion Resistant
316L SS
AT Induced Draft Counterflow Cooling Towers

## Slide 20: Design Advantages – Most Efficient Heat Transfer
EVAPAK® Counterflow Fill:
Even Temperature Gradients through Fill Cross-section
Cools precisely to design temperature
Requires Less Air
Optimal Fill Location
35°C Entering Water Temperature
Entering Air at 25,6°C Wet-Bulb Temperature
30°C Net
Outlet Water
Temperature
34°C
32,5°C
31°C
30°C
Water Temp
Isotherms
AT Induced Draft Counterflow Cooling Towers

## Slide 21: Design Advantages - Optimal Fill Location
Completely encased in steel
Protected from direct exposure
AT Induced Draft Counterflow Cooling Towers

## Slide 22
EVAPAK® Fill
  Removable, bonded block construction
  Low pressure drop
  Bottom supported
Signature Features – Most Efficient Heat Transfer
Counterflow Cooling Towers

## Slide 23: Comparison – Crossflow Heat Transfer
Temperature Gradients Not Uniform Across Fill
Some Water Not Cooled to Design Temperature
Allows air to bypass
Easily clogged, difficult to replace
AT Induced Draft Counterflow Cooling Towers
35°C Entering Water Temperature
35°C
33,5°C
32,2°C
31°C
29,5°C
27,8°C
26,5°C
Entering Air at 25,6°C
Wet-Bulb Temperature
29,4°C Net
Outlet Water
Temperature
Crossflow Fill

## Slide 24
Design Advantages – Winter Operation
18,5°C Entering Water Temperature
Entering Air at -12°C Wet-Bulb Temperature
7,2°C Net
Outlet Water
Temperature
10,5°C
12,8°C
10°C
7,2°C
Temperature Gradients 7,2°C – 0°C = 7,2°C Safety
Unique Inlet Louver Design
Water Temp
Isotherms
AT Induced Draft Counterflow Cooling Towers
Counterflow Fill

## Slide 25: Design Advantages – Winter Operation
Temperature Gradients 1,1°C – 0°C = Greater Great Risk for Ice Formation
Ice Builds on Louvers & Fill
AT Induced Draft Counterflow Cooling Towers
48,5°C Entering Water Temperature
17,8°C
15,5°C
12,7°C
10°C
7,2°C
4,4°C
1,1°C
Entering Air at 10° F
Wet-Bulb Temperature
7,2°C Net
Outlet Water
Temperature
Crossflow Fill

## Slide 26: Design Advantages – Winter Operation
Exposed Crossflow Fill:
Ice Formation
Ice Builds on Louvers & Fill
AT Induced Draft Counterflow Cooling Towers

## Slide 27
Externally Mounted TEFC Motor
Power-Band Adjustment from Outside
Bearing Lubrication Lines Extended to Outside
Simplified Maintenance – Mechanical Drive System
AT Induced Draft Counterflow Cooling Towers
2,4 m Wide Models

## Slide 28
Simplified Maintenance – Mechanical Drive System
Easy-Glide Motor Access Door
Easy Access Fan Belt Adjustment
Locking Mechanism Designed to Adjust Power-Band Belt Tension
AT Induced Draft Counterflow Cooling Towers
3 m, 3,6m and 4,3 m Wide Models

## Slide 29
Simplified Maintenance – Mechanical Drive System
AT Induced Draft Counterflow Cooling Towers
Fan Bearing Lubrication from Outside the Unit
3 m, 3,6m and 4,3 m Wide Models

## Slide 30
Swing Out Motor Base for Easy Service
Simplified Maintenance – Mechanical Drive System
3 m, 3,6m and 4,3m Wide Models
AT Induced Draft Counterflow Cooling Towers

## Slide 31
Swing Out Motor Base for Easy Service
Simplified Maintenance – Mechanical Drive System
3 m, 3,6m and 4,3m Wide Models
AT Induced Draft Counterflow Cooling Towers

## Slide 32
Drift rate less than 0.001% of recirculated water rate
Block sunlight from shining directly in the cold water basin
Significantly better than crossflow drift rate of 0.005%
Signature Features – High Efficiency Drift Eliminators
AT Induced Draft Counterflow Cooling Towers

## Slide 33
Simplified Maintenance – Water Distribution
No Service Necessary from the Fan Deck
Fill Provides Safe Work Area for Maintaining Water Distribution System
AT Induced Draft Counterflow Cooling Towers

## Slide 34
Simplified Maintenance – Water Distribution
EvapJet Nozzles
Wide Opening: Prevent Clogging
Maximize Spray Area: Less Nozzles
Screw in Type
AT Induced Draft Counterflow Cooling Towers

## Slide 35
Pressurized Water Distribution
Single Inlet Piping
Self Balancing – No Valves needed
No Hot Water Distribution Pans
Design Advantages – Water Distribution
AT Induced Draft Counterflow Cooling Towers

## Slide 36: Design Advantages – Operating and Layout Weight
AT Induced Draft Counterflow Cooling Towers

## Slide 37
Simplified Maintenance – Basin Area Access
‘Clean Pan’ Sloped Basin Design
AT Induced Draft Counterflow Cooling Towers

## Slide 38
Design Advantage – Reduced Operating Weight
‘Clean Pan’ Sloped Basin Design
AT Induced Draft Counterflow Cooling Towers
Reduces overall operating weight

## Slide 39
Two Pass Inlet Louver
Basin Enclosed - Not exposed to Wind & Sun
Angled Cross section “Sight-tight” design
Sunlight
Splashout
Debris
Air Intake
Signature Features – Unique Inlet Louvers
AT Induced Draft Counterflow Cooling Towers

## Slide 40
Simplified Maintenance – Basin Area Access
Easily Removable Inlet Louvers for Full Basin Access
Can Be Performed from Outside Unit:
  Float Valve Adjustment
  Remove and Clean Strainers
  Clean Pan Bottom
AT Induced Draft Counterflow Cooling Towers

## Slide 41
Simplified Maintenance – Basin Area Access
AT Induced Draft Counterflow Cooling Towers

## Slide 42
Easy Maintenance – Louver Access Door
Hinged access panel with quick release mechanism.
Allows easy access to perform routine maintenance and inspection of the makeup assembly, strainer screen and basin.
AT Induced Draft Counterflow Cooling Towers

## Slide 43
Standard Stainless Steel Strainers
Simplified Maintenance –Basin Area Access
AT Induced Draft Counterflow Cooling Towers

## Slide 44
Plan Area
Less Tower Area + Less Air = Smaller Plan Area
Net Free Area
Counterflow Tower
360° Air Intake
End Air Intake
Net Free Area
Crossflow
More Tower Area + More Air = Larger Plan Area
Design Advantages – Layout
AT Induced Draft Counterflow Cooling Towers

## Slide 45
Design Advantages – Minimized Recirculation Potential
CROSSFLOW
COUNTERFLOW
AT Induced Draft Counterflow Cooling Towers

## Slide 46
Simplified Maintenance – Accessories
Sloped Ladders
AT Induced Draft Counterflow Cooling Towers

## Slide 47
Simplified Maintenance – Accessories
External Service Platform and Ladder
Motor Davit
Basin Level Platform
AT Induced Draft Counterflow Cooling Towers

## Slide 48: AT Induced Draft Counterflow Cooling Towers
CTI-certified options for reduced sound levels
  Discharge Attenuation
  Low Sound Fan
  Super Low Sound Fan
  Water Silencers
  Offset Inlet Walls
Low Sound Solutions
Notes: Another complementary Low Sound Solution option to reduce sound levels is the new Discharge Attenuator.
(click)

## Slide 49: AT Induced Draft Counterflow Cooling Towers
Discharge Attenuation –Up to 10 dB(A) Reduction
Dimensional Impact
Straight sided discharge hood
Adds 1.400 mm to standard unit height
Construction
High density fiberglass insulated walls and low pressure drop baffling system
Thermal Performance
5% thermal performance derate
Low Sound Solutions
Notes: The discharge attenuation is a straight sided discharge hood, which adds 55 inches (1400mm) to the unit height.
It is designed with high density fiberglass insulated walls, low pressure drop baffling and is self supporting.
There is a 2% thermal performance derate with the addition of the discharge attenuation package.
(click)

## Slide 50: AT Induced Draft Counterflow Cooling Towers
Low Sound Fan – 4 to 7 dB(A) Reduction
Dimensional Impact
Adds 0 mm on most units
Adds 175 mm on large units
Available on all units except 1,2 m wide cells
Construction
Aluminum construction wide chord fan blades with steel fan hub
Thermal Performance
3.5% thermal performance derate
Low Sound Solutions
Notes: The Low Sound Fan offers a 4 to 7 dB(A) reduction.
The Low Sound Fan is available on all 12’ and 14’ wide cells. This option adds 7 inches to cell height.
The Low Sound Fan is a wide chord design which employs aluminum blades and a steel fan hub design.
These features result in a fan able to move the required air flow at reduced fan speed.
Because we’re moving the same amount of air, there is no performance derate!
(click)

## Slide 51: AT Induced Draft Counterflow Cooling Towers
SUPER Low Sound –Fan 9 to 15 dB(A) Reduction!
Dimensional Impact
Adds 330 mm to 530 mm to fan cylinder height
Available on all units except 1,2 m wide
Construction
Molded, heavy duty FRP construction
Extremely wide chord blades
Unique forward swept blade profile
Reduced fan speed
Thermal Performance
No thermal performance derate!
Low Sound Solutions
Notes: The SUPER Low Sound Fan is available on all the 8.5’ wide cells.
This option adds 12 to 21 inches (250 to 530mm) to cell height, depending upon unit size.
SUPER Low Sound Fans are one piece molded construction utilizing heavy duty FRP. Please note, the fan hub is not a separate component.
This leading edge technology incorporates extremely wide chord blades with a unique forward swept blade profile.
This unique fan design results in a fan which is able to move the required air flow at significantly reduced fan speed.
Because we’re moving the same amount of air, there is no performance derate!
(click)

## Slide 52: AT Induced Draft Counterflow Cooling Towers
Water Silencers - 4 to 7 dB(A) Reduction
Dimensional Impact
Available on all standard AT products
No dimensional impact
Construction
Lightweight PVC
Easily removable sections rest on steel supports
Located in the falling water area of the cold water basin
Thermal Performance
No thermal performance derate!
Low Sound Solutions
Notes: Water Silencers are available on all standard AT products.
There is no dimensional impact for this option.
Water Silencers are constructed from lightweight PVC material and are provided in easily removable sections, which rest on steel supports
(CLICK)
Water Silencers are located in the falling water area of the cold water basin.
Because the water silencers are not directly in the air stream, there is no thermal performance derate.
(click)

## Slide 53: AT Induced Draft Counterflow Cooling Towers
Offset Inlet Walls- Typical 7 dB(A) Reduction
Dimensional Impact
Available on all standard AT products
Mounted 1,8 m away from air inlet louvers
Require external steel support (by others)
Used in conjunction with water silencers and SLSF
Construction
Galvanized Steel with acoustically lined baffles
Lateral support members for increased rigidity
Thermal Performance
No thermal performance derate!
Low Sound Solutions
Notes: Water Silencers are available on all standard AT products.
There is no dimensional impact for this option.
Water Silencers are constructed from lightweight PVC material and are provided in easily removable sections, which rest on steel supports
(CLICK)
Water Silencers are located in the falling water area of the cold water basin.
Because the water silencers are not directly in the air stream, there is no thermal performance derate.
(click)

## Slide 54
LSTE
Forced Draft
Counterflow Cooling Towers

## Slide 55: LSTE Models And Nomenclature
Centrifugal Fan Design
10 Box Sizes
145 – 5.930 kW
LSTE Forced Draft Counterflow Cooling Towers

## Slide 56: LSTE Models And Nomenclature
LSTE Forced Draft Counterflow Cooling Towers
LST | - | Low Sound Tower
E | - | Product Version
10 | - | Width of Unit (feet)
5 | - | Capacity Designator
24 | - | Lenght of Unit (feet)
LSTE 10524

## Slide 57
TEFC motors designed for cooling tower applications
Motor mounted outside of unit on adjustable base
Easy to adjust belt tension or change motor
Fan Motors – LSTE 1.6m Wide Towers
LSTE Forced Draft Counterflow Cooling Towers

## Slide 58
TEFC motors designed for cooling tower applications
Motor mounted in open area on adjustable base
Easy to adjust belt tension or change motor
Fan Motors – LSTE 2.4m and 3m Wide Towers
LSTE Forced Draft Counterflow Cooling Towers

## Slide 59
Z-725 Hot-Dip Galvanized Steel
PVC Spray Distribution System
PVC Drift Eliminators
Stainless Steel Strainers
EVAPCO Corrosion Protection System
Standard Materials
LSTE Forced Draft Counterflow Cooling Towers

## Slide 60
304L or 316L Stainless Steel Construction
Different Options:
  Cold Water Basin
  Water Touch Unit
  Complete Construction
Optional Materials of Construction
LSTE Forced Draft Counterflow Cooling Towers

## Slide 61: LSTE Design And Construction
One Piece “Forged Journal” Shaft
  Eliminates “Tack Welded Journals”
  Increases Shaft Life
LSTE Forced Draft Counterflow Cooling Towers

## Slide 62: EVAPAK® Fill – A Working Platform!
Bonded Fill Bundles with Bottom Supports make EVAPAK® Fill an Ideal Working Platform
Provides “Safe” Work Area to Perform Maintenance on Spray Distribution System
LSTE Forced Draft Counterflow Cooling Towers

## Slide 63
Efficient Drift Control – 0,001%
Easy to Handle, Lightweight Framed Sections
Non-Corrosive PVC
PVC Drift Eliminators
LSTE Forced Draft Counterflow Cooling Towers

## Slide 64
Corrosion Resistant
Eliminates Expensive Maintenance Caused by “Corroded” and “Collapsed” Galvanized Strainers
Stainless Steel Strainers
LSTE Forced Draft Counterflow Cooling Towers

## Slide 65: LSTE Design And Construction
PVC Water Distribution System
Non-corrosive Spray Header & Nozzles
Threaded Nozzles Eliminate Troublesome “Rubber Grommets”
Large 25 mm Nozzle Opening and Anti-sludge Ring Reduces Clogging
Self-balancing, Pressurized
Sludge Ring
Debris
LSTE Forced Draft Counterflow Cooling Towers

## Slide 66: LSTE Design Advantages
Indoor Installations with External Static Pressure-Centrifugal Fan Design
Sound-Attenuation Available on Centrifugal Fan Design
LSTE Forced Draft Counterflow Cooling Towers

## Slide 67: LSTE CUSTOMER BENEFITS

## Slide 68
Centrifugal fans
Single sided air entry
Optional intake and discharge attenuation
Very Quiet Operation
LSTE Forced Draft Counterflow Cooling Towers

## Slide 69
Easy access motors
Fan and drive components easily accessible
Large circular access doors located by float valve and strainer assembly
Non-corrosive PVC fill, eliminators, and water distribution system
Fill can be used as working platform
Easy Maintenance
LSTE Forced Draft Counterflow Cooling Towers

## Slide 70
Ducted indoor layouts
Replacement tower
Noise sensitive applications
Low height
Applications
LSTE Forced Draft Counterflow Cooling Towers

## Slide 71
Taking
Quality
and
Service
to a
Higher Level . . .
EVAPCO EUROPE BVBA